## Slide 1
Universal Real-Time Infrastructure Monitoring and Observability Platform
Summer Internship Project executed at ISTRAC, Lucknow, ISRO
INTERN CANDIDATE
Dhruv Rathore KIIT University, B.Tech CSE
PROJECT GUIDE
Shri Anant Madhukar Scientist / Engineer, ISRO
TIMELINE
11 May 2026 — 18 June 2026 6-Week Structural Internship
ISRO • ISTRAC LUCKNOW
Slide 1 / 28
Notes: Good morning respected panel members, scientists, engineers, and mentors. My name is Dhruv Rathore, and I am a third-year Computer Science and Engineering student from KIIT University. During my summer training at ISTRAC, Lucknow, ISRO, under the guidance of Shri Anant Madhukar, I worked on a project titled 'Universal Real-Time Infrastructure Monitoring and Observability Platform.' The project focused on building a distributed monitoring system inspired by tools such as Zabbix, Nagios, Grafana, and Datadog Infrastructure Monitoring.

## Slide 2
About ISTRAC & Operational Scope
• ISTRAC plays an essential role in ISRO mission operations by offering Tracking, Telemetry, and Command (TTC) services.
• Distributed ground control pipelines, payload datastores, and server operations comprise these capabilities.
• Maintaining maximal availability (99.999% uptime) of infrastructure is critical to avoid mission lag or interruption.
• Real-time monitoring helps catch node bottlenecks, daemon crashes, and disk failures before service degradation occurs.
TRACKING
Antenna path positioning & telemetry polling.
TELEMETRY
Retrieving data variables from vehicles & satellites.
COMMAND
Uplinking mission controls securely from ground blocks.
ISRO • ISTRAC LUCKNOW
Slide 2 / 28
Notes: ISTRAC plays a central role in ISRO's mission support activities by providing tracking, telemetry, and command services. These operations depend on distributed technical infrastructure such as servers, network devices, applications, and communication systems. In such environments, infrastructure visibility is important because small faults can affect larger operational workflows. This project was aligned with that need by exploring how a unified monitoring platform can provide real-time visibility into system health.

## Slide 3
The Infrastructure Monitoring Problem
• Heterogeneous ecosystems consist of mixed Linux kernels, legacy systems, and database daemons, blocking unified operations.
• Information silos restrict observability because engineers must query separate CLI outputs or local journals.
• Manual server audits do not scale when dealing with dozens of active telemetry servers.
• Delayed fault detection raises operational risk during mission-critical telemetry windows.
CURRENT INFRASTRUCTURE SILOS:
• Isolated Windows Servers and VM instances
• Separate container orchestration environments
• No shared threshold mapping engine
• Risk of cascading outages due to slow triage cycles
ISRO • ISTRAC LUCKNOW
Slide 3 / 28
Notes: The problem addressed in this project is the lack of a single monitoring interface for heterogeneous infrastructure. In technical environments, different hosts may run Windows, Linux, containers, databases, and network services. If each is checked separately, engineers lose time correlating information. A monitoring platform must collect metrics continuously, evaluate thresholds, and present a common operational view.

## Slide 4
Project Objectives & Core Deliverables
30s
Target Metric Ingestion Window
Continuous sampling of CPU, RAM, disk allocations, processes, and service states across Windows and Linux hosts.
• Create a Zabbix-style lightweight infrastructure monitoring solution.
• Build a custom host agent with no dependencies to run natively.
• Construct a distributed processing pipeline with Apache Kafka as a buffer queue.
• Deconstruct telemetry storage into a PostgreSQL state store and ClickHouse analytical store.
• Introduce threshold-based alert rules that open, acknowledge, and resolve problems automatically.
ISRO • ISTRAC LUCKNOW
Slide 4 / 28
Notes: The objective was to build a working full-stack monitoring platform from scratch. The system collects CPU, memory, disk, network, process, service, and uptime metrics from monitored machines. These metrics pass through a Kafka-based processing pipeline and are stored in PostgreSQL and ClickHouse. The dashboard provides live host status, metric charts, alert rules, and problem management.

## Slide 5
Six-Week Development Timeline
PHASE 1: EVENT INGESTION (WEEKS 1 - 3)
• Constructed raw stream parser supporting multi-format JSON, CSV, and XML pipelines.
• Built ingestion gateway decoupled with Apache Kafka broker.
• Implemented real-time data streaming using JWT security patterns.
• Delivered telemetry variables to live dashboard through WebSockets.
PHASE 2: PLATFORM EVOLUTION (WEEKS 4 - 6)
• Transitioned into full-scale, structured Zabbix-style metric monitor.
• Engineered lightweight, zero-dependency Node.js client agent.
• Configured dual-database strategy (PostgreSQL & ClickHouse).
• Created custom threshold alerting model and interactive Next.js dashboard.
ISRO • ISTRAC LUCKNOW
Slide 5 / 28
Notes: The internship progressed in two phases. During the first three weeks, I built a universal real-time event ingestion platform inspired by Splunk and Elasticsearch. This established the core distributed architecture: ingestion, Kafka, processing, storage, authentication, WebSocket delivery, and dashboarding. In the final three weeks, the system evolved into an infrastructure monitoring platform with agents, metrics, alert rules, problems, and a Zabbix-style interface.

## Slide 6
Phase 1: Universal Ingestion Architecture
• Format-Agnostic Ingestion Engine: Handled high-throughput logs containing mixed structures (Syslog, CSV, Key-Value) without upfront schema constraints.
• Asynchronous Processing Pipeline: Separated network listener components from database operations using Kafka.
• JWT-Secured Node Boundaries: Protected microservice communication paths with token verification routines.
PHASE 1 PIPELINE TOPOLOGY
[Log Source] -> [HTTP Gateway] | v [Kafka Buffer] | v [Token Parser] | v [PostgreSQL] ----- [Redis PubSub] | v [Live Dashboard]
ISRO • ISTRAC LUCKNOW
Slide 6 / 28
Notes: Phase 1 was not discarded. It formed the technical base for the final system. It proved that the architecture could ingest data, process it asynchronously, persist it, and stream updates to the browser in real time. The format-agnostic parser was important because it handled multiple data formats without prior schema knowledge. This experience helped define the later monitoring data pipeline.

## Slide 7
Strategic Pivot: Logs to Metrics
PHASE 1: LOG ANALYTICS
• Raw event lines provide audit trails but lack host performance indicators.
• Assessing rapid memory leakage, swap performance, or disk limits is slow.
• Relies heavily on CPU-intensive regular expressions for metrics extraction.
PHASE 2: STRUCTURED INFRASTRUCTURE METRICS
• Standardized JSON payload models host health directly.
• Reused the proven high-throughput Kafka-Express messaging gateway.
• Integrated sub-second alerting and problem-state management in database.
ISRO • ISTRAC LUCKNOW
Slide 7 / 28
Notes: The pivot from log analytics to infrastructure monitoring was an engineering decision based on the project's operational relevance. Phase 1 validated the pipeline, but monitoring required a more structured model around hosts, metrics, services, and alert rules. Instead of treating the pivot as a restart, I treated it as an architectural evolution. The same concepts of ingestion, processing, storage, and real-time delivery were adapted to monitoring.

## Slide 8
Final System Architecture Pipeline
• Node.js Host Agent: Pulls resource metrics locally and runs shell tasks across OS types.
• Kafka Ingestion Broker: Buffers REST gateway traffic, preventing data loss during agent spikes.
• Dual Storage Strategy: Stores active problems in PostgreSQL and registers time-series series in ClickHouse.
• Real-time Pipeline: Delivers events via Redis PubSub straight to the WebSocket client.
DATA PIPELINE SCHEMATIC
[Host Agent] -> API Ingestion Gateway (:4000) | v [Kafka Broker] | v [Metrics Processor] | +---------------+--------------+ | | v v [PostgreSQL State] [ClickHouse Storage] | v [Redis PubSub] -> [WS Gateway] -> [UI]
ISRO • ISTRAC LUCKNOW
Slide 8 / 28
Notes: This is the final architecture. The monitoring agent runs on each monitored machine and sends heartbeats every 10 seconds and full metric check-ins every 30 seconds. The Agent API validates the agent key and publishes the payload to Kafka. The Metrics Processor stores data, evaluates alerts, updates host status, and publishes live events through Redis. The WebSocket Gateway then delivers updates to the browser dashboard.

## Slide 9
Technology Stack Selection Matrix
Infrastructure Layer | Selected Technology | Core Engineering Rationale
Runtime | Node.js 20 (LTS) | Event-driven asynchronous framework ideal for handling high I/O volumes.
API Layer | Fastify Framework | Extremely fast, lower-overhead alternative to traditional Express.
Frontend Portal | Next.js 14 & React | Robust React-based framework for server-rendered user state.
Message Broker | Apache Kafka | High-throughput log stream that acts as a secure landing area for metrics.
Relational DB | PostgreSQL 16 | Used for transactional relational integrity (rules, states, active alarms).
OLAP Database | ClickHouse 23.8 | Fast column-oriented analytic store for high-volume metric trends.
In-Memory Store | Redis 7 | Extremely fast cache memory; handles transient websocket messaging.
Websockets | Socket.io | Abstracts cross-browser connections and manages active client pipelines.
Metric Charts | Recharts Components | Highly responsive declarative graphs compatible with Next.js dashboards.
Infrastructure | Docker & Compose | Encapsulates environments inside standardized containers for deployment.
ISRO • ISTRAC LUCKNOW
Slide 9 / 28
Notes: Each technology was selected for a specific role. PostgreSQL stores relational data such as users, hosts, sessions, alert rules, and problems. ClickHouse stores high-volume time-series metric readings. Kafka decouples agent ingestion from processing, while Redis provides low-latency pub/sub for dashboard updates. Next.js and Recharts were used to build a professional monitoring dashboard.

## Slide 10
Microservices Architectural Design
Microservice Name | Port Assignment | Architectural Role | Service Responsibility
agent-api | Port 4000 | Ingestion Boundary | Authenticates external client requests; publishes parsed metrics directly to Kafka.
auth-api | Port 4002 | Control Plane Service | Manages credentials, registers host configurations, and handles manual alerts.
metrics-processor | Internal Daemon | Queue Consumer | Reads from the message broker, executes alerts, and coordinates DB writes.
ws-gateway | Port 4001 | Real-Time Broadcaster | Maintains active client connections and broadcasts live status changes.
monitoring-agent | Local Client | Hardware Collector | A client script that executes OS-level queries and uploads JSON payloads.
ISRO • ISTRAC LUCKNOW
Slide 10 / 28
Notes: The backend is split into focused services. Agent API handles external agent traffic. Auth API serves the dashboard and manages authentication. Metrics Processor runs as a Kafka consumer and performs storage and alert evaluation. WebSocket Gateway handles real-time delivery. The monitoring agent runs on the monitored machine and has no npm dependencies.

## Slide 11
Database Design: PostgreSQL & ClickHouse
POSTGRESQL 16: STATE ENGINE
• Structured tables: users, hosts, alert rules, active problems, metric configurations.
• Monthly partition models on system readings prevent storage growth from affecting queries.
• Leverages native database JSONB fields to house host metadata, alerting rules, and contacts.
CLICKHOUSE: ANALYTICS STORE
• A highly efficient column-oriented store designed for large analytical datasets.
• Raw telemetry values are stored using schemas with custom delta compression.
• Materialized views automate background computations for hourly and daily trend graphs.
ISRO • ISTRAC LUCKNOW
Slide 11 / 28
Notes: The database design uses two stores because monitoring data has two different access patterns. PostgreSQL is used for structured operational state, including users, hosts, alert rules, problems, and services. Metric readings are also stored in PostgreSQL for recent access and partitioned monthly. ClickHouse is used for analytical time-series queries and rollups, which are better suited to historical charts and reports.

## Slide 12
The Zero-Dependency Host Agent
• Written in plain JavaScript using built-in Node.js libraries (os, fs, child_process, net, http).
• Zero reliance on third-party packages, preventing module drift and security risks.
• Calculates CPU performance by measuring multi-core scheduler loops over 100ms periods.
• Abstracts OS differences by routing queries through platform-specific CLI loops.
• Monitors TCP ports directly to verify database, web, and internal network services.
AGENT RUNTIME PROCESS
[Start Lifecycle] | v [Verify Security Keys] -> [Register with Core API] | +--------------------------+--------------------------+ | (T = 10s) | (T = 30s) v v [Send Heartbeat Payload] [Query Hardware Metrics] | | (CPU, Disk, Net) | v +--------------------------<------------------ [Assemble & Post JSON] | v [Retry with Backoff on Fail]
ISRO • ISTRAC LUCKNOW
Slide 12 / 28
Notes: The monitoring agent is one of the most important components of the project. It was written in plain JavaScript using only built-in Node.js modules such as os, fs, http, https, child_process, and net. CPU usage is calculated by sampling CPU times twice with a short gap. Disk and network collection differ between Windows and Linux, so the agent uses platform-specific commands and parsing logic.

## Slide 13
Intelligent Alert Engine Lifecycle
• Evaluates metric values against rule-defined parameters in the Metrics Processor daemon.
• Creates a new PostgreSQL problem record with timestamp if a metric breaches a threshold.
• Maintains existing problem states during continued failures, avoiding duplicate records.
• Resolves problems automatically and records timestamps as metrics return to normal ranges.
ALERT ENGINE STATE TRANSITIONS
+-----------------------+ | METRIC WITHIN RANGE | <-----------------+ +-----------------------+ | | | | [Threshold Breached] | [Metric Clears] v | +-----------------------+ | | PROBLEM CREATED | | +-----------------------+ | | | | [Acknowledge Action] | v | +-----------------------+ | | ACKNOWLEDGED INCIDENT | ------------------+ +-----------------------+
ISRO • ISTRAC LUCKNOW
Slide 13 / 28
Notes: The alert engine follows a trigger model similar to Zabbix. Each metric is compared against enabled alert rules. If a threshold is breached and no active problem exists, a new problem is opened. If the same problem already exists, its value and severity can be updated. When the metric returns to normal, the problem is automatically resolved. Users can also acknowledge active problems.

## Slide 14
Low-Latency Live Delivery Flow
• Agent posts system metrics directly to the API ingestion path.
• Ingestion layer publishes raw payload string inside a Kafka queue.
• Metrics Processor evaluates rules and posts updates to Redis.
• WebSocket Gateway broadcasts events directly to open browser rooms.
• Next.js dashboard components redraw immediately without page refreshes.
• Validated overall latency: under 2 seconds across active endpoints.
ISRO • ISTRAC LUCKNOW
Slide 14 / 28
Notes: Real-time delivery is handled through a chain of asynchronous components. The agent does not communicate directly with the dashboard. It sends data to Agent API, which publishes to Kafka. Metrics Processor consumes the message and publishes live events to Redis. WebSocket Gateway subscribes to Redis and emits updates to browser rooms. During validation, updates reached the dashboard in under two seconds.

## Slide 15
Dashboard Overview
• High-density dashboard design, engineered for continuous operations centers.
• Features clean cards to trace metrics including CPU, RAM, and Disk storage.
• Maintains interactive active problems logs with manual alert acknowledgement tools.
• Integrates historical time-series analytics charts using high-performance queries.
MONITORING UI ARCHITECTURE
+------------------------------------------------------+ | [Global Health Status Overview Row] | +------------------------------------------------------+ | Host Inventory Grid | Active Trigger Alarms Panel | | | | | * LUC-GW-SRV-01 [OK] | * CPU Overload (>90%) [WARN]| | * LKO-DB-SRV-02 [WARN] | * Disk Full (>95%) [CRIT] | +------------------------------------------------------+ | Real-time System Gauges & Live Stream Activity Logs | +------------------------------------------------------+
ISRO • ISTRAC LUCKNOW
Slide 15 / 28
Notes: The dashboard was redesigned as an enterprise monitoring console rather than a decorative web page. A light theme was selected because tools used in operations environments usually prefer readability and dense tables. The overview page shows host health, active problems, and live updates. Host detail pages show gauges, service status, historical charts, and problem history.

## Slide 16
LIVE DEMONSTRATION
Operational Platform Demo: Launching local agent loops, inspecting ingestion logs, viewing dashboard state updates, and triggering dynamic rules
ISRO • ISTRAC LUCKNOW
Slide 16 / 28
Notes: I will now move to the live demonstration. The demo will show the monitoring agent running locally, sending metric check-ins to the backend pipeline. Then I will show the dashboard updating with live host metrics. Finally, I will demonstrate the alert workflow by showing a problem being created and then acknowledged or resolved.

## Slide 17
Agent Payload & Metrics Format
SAMPLE CLIENT TELEMETRY PAYLOAD
{ "agent_key": "ak_istrac_luc_01", "hostname": "LUC-GW-SRV-01", "metrics": { "cpu_usage": 42.18, "ram_total_mb": 16384, "ram_used_mb": 8192, "disk_total_gb": 512, "disk_used_gb": 256, "uptime_secs": 86400, "services_state": { "ssh": 1, "postgres": 1 } } }
• Agent Heartbeats: Dispatches lightweight heartbeat status pings every 10 seconds.
• Full Metrics Payloads: Packages complete telemetry fields for ingestion every 30 seconds.
• Idempotent Validation: Confirms system registrations securely via unique API keys.
• Backoff Recovery: Retries communication using exponential backoffs if endpoints fail.
ISRO • ISTRAC LUCKNOW
Slide 17 / 28
Notes: This slide represents what the monitoring agent sends to the backend. The actual payload contains CPU, memory, disk, network, load average, uptime, process count, and service checks. The agent sends heartbeats more frequently than full metric payloads so the platform can detect stale or offline hosts. If the backend is unavailable, the agent retries using exponential backoff.

## Slide 18
Dashboard Real-Time Updates
• Instant Gauge Sweeps: Visual progress bars update instantly when metrics change.
• System Status Badges: Color elements switch dynamically to show status states (OK, WARN, CRIT).
• Real-time Alerts Panel: Rule breaches render notifications without requiring page refreshes.
• On-Demand Charts: Graph coordinates pull cleanly from time-series storage arrays.
ISRO • ISTRAC LUCKNOW
Slide 18 / 28
Notes: During the dashboard demo, the important point is that updates are pushed from the backend rather than pulled manually by the user. The WebSocket connection receives metric updates and host status changes. When an alert rule is breached, the problem list updates. Historical charts are loaded through REST APIs, while live readings arrive through WebSocket events.

## Slide 19
Achievement 1: Multi-Host Monitoring
• Validated Concurrent Ingestion: Successfully processed streams from multiple active hosts without database locks.
• Aggregated Health Overview: Created a status interface mapping active hosts, open problems, and hardware usage metrics.
• Host Isolation Safeguards: Assured secure tenant boundaries by tying streams to unique system API keys.
MULTI-HOST TELEMETRY PIPELINE
[Host Node A] --(ak_luc_01)-------+ | [Host Node B] --(ak_luc_02)-------+-----> [CORE API GATEWAY] | | [Host Node C] --(ak_luc_03)-------+ v [KAFKA QUEUE] | v [METRICS DECOUPLER] | v [UNIFIED DASHBOARD]
ISRO • ISTRAC LUCKNOW
Slide 19 / 28
Notes: The first major achievement is simultaneous multi-host monitoring. Each host has its own agent key and sends its own metric stream. The backend maps the agent key to a host record and tenant. This allows the dashboard to show all hosts together while still preserving host-specific metrics, problems, services, and history.

## Slide 20
Achievement 2: Alert Lifecycle Loops
INCIDENT TRIGGER STATE
• Monitored CPU load crosses the 90% threshold for over two intervals.
• Alert parser validates parameters and records a new active incident.
• Alters host health states in the dashboard UI within two seconds.
AUTOMATED RESOLVE STATE
• CPU usage level drops below the configured trigger value.
• Alert parser updates PostgreSQL records automatically.
• Clears issues from the active dashboard immediately without manual intervention.
ISRO • ISTRAC LUCKNOW
Slide 20 / 28
Notes: The second major achievement is alert automation. I validated that when a metric crosses a configured threshold, the alert engine creates a problem record. The dashboard shows this as an active problem. If the metric returns to a normal value, the engine resolves the problem automatically. This closely follows the operational workflow used in monitoring systems.

## Slide 21
Addressing Technical Challenges
Observed Engineering Challenge | Root Cause Analysis | Selected Resolution & Implementation
ClickHouse Driver ESM Crash | Conflict between modern ES Module (ESM) libraries and legacy CommonJS setups. | Structured tsconfig parameters to support standard module exports during runtime.
Kafka Duplicated Topics Error | Broker restarts raised error warnings because existing configurations remained in Zookeeper. | Added pre-creation check routines to verify if topics already exist before making requests.
Cross-Platform Parsing Errors | Windows and Linux systems formats CLI reports differently for disk/network stats. | Built distinct OS-specific parser commands inside the host agent scripts.
ISRO • ISTRAC LUCKNOW
Slide 21 / 28
Notes: Several practical engineering issues appeared during implementation. ClickHouse client integration required attention because of module compatibility with CommonJS TypeScript. Kafka topic creation also needed to be handled safely because restarts can leave state in Zookeeper. The monitoring agent required separate collection logic for Windows and Linux, especially for disk and network metrics.

## Slide 22
Core Engineering Decisions & Logic
Design Choice | Alternative Evaluated | Selected Engineering Rationale
Kafka Ingestion Buffer | Direct Database Writing | Protects primary databases from packet losses during mass client restarts.
ClickHouse for Metrics | PostgreSQL-Only Setup | ClickHouse optimizes analytical storage footprint and queries for massive trends.
Fastify Framework | Standard Express.js Engine | Delivers higher throughput and lower memory overhead for high API volumes.
Redis PubSub Events | Database Polling Logic | Allows direct messaging to web clients without database performance penalties.
Agent-Based Monitoring | Agentless SNMP Only | Provides better local security control and accurate resource diagnostics.
ISRO • ISTRAC LUCKNOW
Slide 22 / 28
Notes: This slide summarizes important design decisions. Kafka was used to separate agent ingestion from processing, which prevents slow database writes from blocking agent requests. ClickHouse was added because time-series analytics have different performance needs than relational state. Fastify was used for REST APIs, and Redis PubSub was selected for live delivery instead of polling the database.

## Slide 23
Results Achieved & Validated
• Validated Multi-Platform Agent: Collected OS-level metrics across different machines.
• Stable Ingestion Pipeline: Ingested and processed metrics through Kafka.
• Sub-2s Web Client Updates: Handled websocket pushes in under 2 seconds.
• Integrated Dual DB Strategy: Validated both state storage and time-series writing.
• Automated Alert Lifecycle: Confirmed warning and critical problem workflows.
• Dynamic Ingestion Control: Built stable, format-agnostic payload processors.
ISRO • ISTRAC LUCKNOW
Slide 23 / 28
Notes: The project produced a working prototype with validated end-to-end behavior. The agent collects and sends metrics, Kafka transports them, Metrics Processor stores them, and the dashboard displays them live. Both relational and time-series storage paths were tested. Alert behavior was also validated by breaching and clearing thresholds.

## Slide 24
Comparison with Enterprise Zabbix
Monitoring Capabilities | Enterprise Zabbix Platform | This Platform Prototype
Host Hardware Agent | Yes (Native compiled binary targets) | Yes (Lightweight zero-dependency Node.js client)
Alert Trigger Engine | Yes (Complex expression syntax mapping) | Yes (Simple parameter check-ins)
Alert Lifecycle Management | Yes (Active alerts overview board) | Yes (Dashboard active problems list)
Real-Time Dashboard updates | Yes (Often uses polling configurations) | Yes (Direct WebSocket streaming updates)
Host Autodiscovery Engine | Yes (IP and SNMP subnet scans) | Planned for future roadmap stages
Agentless SNMP Monitoring | Yes (Comprehensive poller system) | Planned for future roadmap stages
ISRO • ISTRAC LUCKNOW
Slide 24 / 28
Notes: This project is not a replacement for Zabbix, which is a mature production tool. The comparison shows that the prototype implements the core monitoring ideas: hosts, agents, metrics, alert rules, problems, and charts. Some advanced features such as SNMP monitoring and auto-discovery were kept out of scope because of the internship duration. The purpose was to build and validate the architecture.

## Slide 25
Platform Prototype Limitations
• No High-Scale Load Testing: Has not been stress-tested under loads representing hundreds of active host connections.
• Lacks Agentless Auditing: No current support for agentless polling via SNMP or ping scans.
• No Out-of-Band Alerts: Out-of-band notifications (SMS, Email, Slack integrations) are not built-in.
• Manual Configuration Model: Adding hosts and updating alert rules requires manual database configurations.
ISRO • ISTRAC LUCKNOW
Slide 25 / 28
Notes: The limitations are mostly scope decisions. The system was validated functionally and with multiple hosts, but formal load testing at production scale was not performed. The current monitoring model is agent-based. SNMP, email and SMS notifications, Kubernetes deployment, and network auto-discovery are natural extensions but were not implemented within the internship duration.

## Slide 26
Platform Architecture Future Roadmap
Proposed Development Extension | Complexity Rating | Strategic System Utility
Kubernetes Deployments | Medium Complexity | Eases scaling by running containerized backend services in clustered clouds.
SNMP Poller Framework | High Complexity | Brings support for agentless network hardware (routers, switches, firewalls).
Operational Alerts Channels | Medium Complexity | Forwards high-priority warnings to operators via Slack, emails, or SMS gateways.
Autonomous Host Discovery | High Complexity | Reduces manual setup tasks by scanning network subnets for active agents.
Production Scale Load Tests | Medium Complexity | Traces capacity limits and identifies message queue or database bottlenecks.
ISRO • ISTRAC LUCKNOW
Slide 26 / 28
Notes: The roadmap focuses on turning the prototype into a larger operational system. Load testing would establish capacity limits. SNMP would allow agentless network device monitoring. Email and SMS would complete notification channels. Kubernetes deployment would improve deployment flexibility, while auto-discovery would reduce manual host registration.

## Slide 27
Core Internship Lessons Learned
STRICT INTER-SERVICE DATA CONTRACTS
• Unambiguous payload schemas prevent processing crashes in async message brokers.
• System decoupling is critical to prevent cascading pipeline blockages.
HYBRID STORAGE STRATEGY
• A single database pattern cannot optimally serve both structured states and high-volume metrics.
• Relational engines are best for states, while columnar stores excel at analytics.
CROSS-PLATFORM COMPATIBILITY
• OS command patterns differ significantly, requiring modular agent designs.
• Thorough validation is key to discovering edge-case runtime failures.
ISRO • ISTRAC LUCKNOW
Slide 27 / 28
Notes: This project taught me that distributed systems depend heavily on clear contracts between services. I also learned that monitoring systems cannot rely on one database pattern for every workload. Current state, historical metrics, alerts, and live updates each need different handling. The project also showed me how early architectural work can be reused when requirements evolve.

## Slide 28
Thank You!
Universal Real-Time Infrastructure Observability Platform Summer Internship Project — ISTRAC, Lucknow, ISRO
Presenter: Dhruv Rathore | Project Guide: Shri Anant Madhukar
Questions & Discussions
ISRO • ISTRAC LUCKNOW
Slide 28 / 28
Notes: To conclude, this internship project resulted in a working infrastructure monitoring platform built from scratch. It includes a monitoring agent, microservices, Kafka processing, PostgreSQL and ClickHouse storage, alert evaluation, WebSocket live delivery, and a professional dashboard. The work is best understood as a prototype with production-grade architectural patterns. Thank you for your time. I will be happy to answer your questions.